## Slide 1: WhammyPlug
POLITECNICO DI MILANO

## Slide 2: Project’s goal
POLITECNICO DI MILANO
This project aims at reproducing the Whammy Pedal functioning, thus, it implements a Pitch Shifter;
The pitch shift technique allows to change the pitch of the input audio signal without changing its original tempo;
The pitch shifting operation is implemented on the two channels of the input audio signal, therefore each channel is treated as mono;
The project is implemented using the Juce framework for audio plugins.

## Slide 3: User Interface
POLITECNICO DI MILANO

## Slide 4: Knob and Buttons
POLITECNICO DI MILANO
The black knob on the left can be used to select one of the possible intervals indicated on the buttons;
As the user turns the knob, one button will become yellow, meaning that the corresponding interval is selected;
By turning the knob clockwise the values go from an octave to a negative octave;
The selection of an interval is used to set the maximum number of semitones that the pitch shifting operation will reach.

## Slide 5: Pedal Slider
POLITECNICO DI MILANO
This slider is meant to act as a pedal;
Once the user has set the maximum interval for the pitch shift operation, the input signal will be modified according to the movement of this slider;
The slider moves from 0 semitones (meaning we are going to hear the original signal) to the number of semitones corresponding to the maximum pitch interval chosen with the knob.

## Slide 6: SoundTouch Library
POLITECNICO DI MILANO
SoundTouch is a C++ library for time and pitch scaling;
It should be capable of processing interleaved stereo blocks, in actual facts, though, the result isn’t satisfying. That’s why we went through the dual-mono path;
Pitch scaling is implemented combining time-scaling (implemented with SOLA algorithm) and resampling:

## Slide 7: DAW & Requirements
POLITECNICO DI MILANO
This project can be used as a standalone application or as a VST plugin for a DAW;
In order for the standalone app to process an input audio signal, it is necessary to use a system for audio routing (like SoundFlower for MacOS, or Virtual Audio Cable for Windows);
This approach allows to route the input audio signal to the application, that then sends the output to the speakers.

## Slide 8: Demo 1
POLITECNICO DI MILANO

## Slide 9: Report 1 – Test signal
POLITECNICO DI MILANO

## Slide 10: Report 1 – Test signal +8th interval
POLITECNICO DI MILANO

## Slide 11: Report 1 – Test signal +5th interval
POLITECNICO DI MILANO

## Slide 12: Report 1 – Test signal -3rd interval
POLITECNICO DI MILANO

## Slide 13: Report 1 – Test signal -6th interval
POLITECNICO DI MILANO

## Slide 14: Improvements
POLITECNICO DI MILANO
To improve the quality of the output signal, interpolation and smoothing were introduced;
The type of interpolation that is used is the Lagrange Interpolation;
This kind of interpolation performs a linear combination of Lagrange basis functions of the input samples, in order to find the polynomial of lowest possible degree that passes through the points of the dataset (in this case, the audio samples).

## Slide 15: Improvements
POLITECNICO DI MILANO
The smoothing is applied, instead, to the slider, in order to attenuate clicks related to the continuous variation of the pitch;
The smoothing consists in applying a ramp envelope to the slider movement, in order to have a gradual change of pitch, and avoid abrubt variations.

## Slide 16: Demo 2
POLITECNICO DI MILANO

## Slide 17: Report 2
POLITECNICO DI MILANO

## Slide 18: Conclusions
POLITECNICO DI MILANO
The improvements tend to decrease the temporal density of the artifacts;
Indeed, it is possible to notice that the transitions between different pitch values are smoother with respect to the ones of the first reports;
It is possible that due to the mediocre quality of the recorder, the recording varies according to the signal level, and some results are not as satisfying as expected.